VEHICLES 1
HYPER6 SLV
lonx -120.49 //Vehicle longitude - deg module newton
latx 34.68 //Vehicle latitude - deg module newton
alt 100 //Vehicle altitude - m module newton
dvbe 1 //Vehicle geographic speed - m/s module newton
phibdx 0 //Rolling angle of veh wrt geod coord - deg module kinematics
thtbdx 60 //Pitching angle of veh wrt geod coord - deg module kinematics
psibdx 180.0 //Yawing angle of veh wrt geod coord - deg module kinematics
alpha0x 0 //Initial angle-of-attack - deg module newton
beta0x 0 //Initial sideslip angle - deg module newton
//environment
mair 0 //'int' mair =|matmo|mturb|mwind| module environment
WEATHER_DECK weather_deck_Wallops.asc
RAYL dvae 5 //Magnitude of constant air speed - m/s module environment
twind 1 //Wind smoothing time constant - sec module environment
turb_length 100 //Turbulence correlation length - m module environment
turb_sigma 0.5 //Turbulence magnitude (1sigma) - m/s module environment
//aerodynamics
maero 13 //'int' =11: last stage; =12: 2 stages; =13: 3 stages module aerodynamics
AERO_DECK aero_deck_SLV.asc
xcg_ref 8.6435 //Reference cg location from nose - m module aerodynamics
refa 3.243 //Reference area for aero coefficients - m^2 module aerodynamics
refd 2.032 //Reference length for aero coefficients - m module aerodynamics
alplimx 20 //Alpha limiter for vehicle - deg module aerodynamics
alimitx 5 //Structural limiter for vehicle - g's module aerodynamics
//propulsion
mprop 3 //'int' =0:none; =3 input; =4 LTG control module propulsion
vmass0 48984 //Initial gross mass - kg module propulsion
fmass0 31175 //Initial fuel mass in stage - kg module propulsion
//	xcg_0 10.53 //Initial cg location from nose - m module propulsion
xcg_0 7.02 //Initial cg location from nose - m module propulsion
//	xcg_0 5.50 //Initial cg location from nose - m module propulsion
//	xcg_1 3.20 //Final cg location from nose - m module propulsion
xcg_1 6.98 //Final cg location from nose - m module propulsion
//	xcg_1 6.76 //Final cg location from nose - m module propulsion
moi_roll_0 21.94e3 //Roll MOI of vehicle, initial - kgm^2 module propulsion
moi_roll_1 6.95e3 //Roll MOI of vehicle, burn-out - kgm^2 module propulsion
moi_trans_0 671.62e3 //Transverse MOI of vehicle, initial - kgm^2 module propulsion
moi_trans_1 158.83e3 //Transverse MOI of vehicle, burn-out - kgm^2 module propulsion
//	moi_trans_0 71.62e3 //Transverse MOI of vehicle, initial - kgm^2 module propulsion
//	moi_trans_1 58.83e3 //Transverse MOI of vehicle, burn-out - kgm^2 module propulsion
spi 279.2 //Specific impulse - sec module propulsion
fuel_flow_rate 514.1 //Fuel flow rate of rocket motor - kg/s module propulsion
END